FORKLIFT SAFETY PROGRAM (FSP)

REACH TRUCK/ORDER PICKER WRITTEN EXAMINATION

I. Multiple Choice Questions Section Instructions-- Read each question CAREFULLY and then circle the letter of the MOST CORRECT answer from the choices below.

- What are the five parts of the visual inspection of the Operator’s Daily Checklist?

A.  paint job, seat covers, brakes, horn, load center

B.  tires, battery, lift/lower system, controls, general safety

C.  controls, center of gravity, brakes, load limit, steering

D.  horn, steering, directional/speed control, lift/lower system, brakes

- What are the six parts of the operational inspection of the Operator’s Daily Checklist ?

A.  paint job, seat covers, brakes, horn, load center, load limit

B.  tires, battery, lift/lower system, controls, general safety, hour meter

C.  controls, center of gravity, brakes, load limit, steering, battery

D. horn, steering, directional/speed control, lift/lower system, brakes, general safety

- What is the best way to minimize the effects of centrifugal force in a turn ?

A.  Accelerate as quickly as possible.

B.  Speed up when apporaching the turn.

C.  Make the turn as sharply as possible.

D.  Make the turn slowly.

- What should you do if your supervisor walks under an elevated load ?

A.  Nothing, because your supervisor should know better.

B.  Begin to lower the load.

C. Get off the truck, walk over to your supervisor, and politely ask him or her to move.

D.  Stop moving and ask your supervisor to move immediately.

- What is the best way to minimize the effects of momentum when starting and stopping a truck ?

A.  Accelerate as quickly as possible.

B.  Face away from the load.

C.  Lean towards the direction of travel.

D.  Avoid sudden starts and stops.

II. TRUE OR FALSE (Circle T or F whichever is more correct)

- When stopping in an emergency, the operator should first release the deadman pedal.	T  F

- When you complete the Operator’s Daily Checklist, part of the battery check is ensuring that the battery is fully charged.  If it isn’t, the battery should be recharged immediately.	T  F

- When a load is elevated, the combined center of gravity will move down. 	T  F

- The horn is a 360 degree warning device to others nearby.  	  	T  F

- The load capacity is the maximum weight that can be carried safely at a designated load center and elevated height.		T  F

- Before raising the mast, you should check overhead for sprinkler heads, beams or other obstructions.		T  F

- If you have just moved forward to pick up a load and are sure that the path is clear, you don’t have to look behind you when you back up.		T  F

- If you took a sharp left turn, centrifugal force will cause the center of gravity to shift to the right momentarily.		T  F

- Always yield to pedestrians.		T  F

- If you operate an order picker, you must wear a safety harness.		T  F

- It is okay to drive up to other employees standing next to the racking if they are there to help you load your truck.	 	T  F

- Forks should be placed under the load as far as possible, and if the truck is equipped with mast tilt or fork tilt, the load should be slightly tilted.		 T  F

- You must carry a load as low as possible to increase stability; however, if you are traveling without a load, you do not need to worry about the level of your forks. 		T  F

- A truck may lose its balance when a load is too heavy or when the load is carried too far from the shank of the forks.		T  F

- When you cannot safely see over a load, you should turn around, face away from the load and drive in that direction.		T  F