FORKLIFT SAFETY PROGRAM (FSP)

STANDARD FORKLIFT WRITTEN EXAMINATION

I. Multiple Choice Questions Section Instructions-- Read each question CAREFULLY and then circle the letter of the MOST CORRECT answer from the choices below.

- Where is the fulcrum (balancing point) located on a sit-down counter-balanced forklift?

A.  rear axle

B.  front axle

C   center of the forklift

D.  center of the forks

- The rear end steering of forklifts:

A.  causes the rear end to swing more than an automobile.

B.  is about the same as an automobile.

C.  the rear end swings less than an auto.

D.  allow the forklift to take sharp turns at high speed.

- When you are traveling with a load on a level surface, the forks should be raised:

A.  at least 12 inches.

B.  between 12 and 18 inches.

C.  no more than 6 inches.

D.  high enough so the operator can see under the load while driving.

- When parking the forklift to go to the bathroom, you should:

A.  Turn the power off and set the parking brake.

B.  Bring the mast forward to the vertical position.

C.  Drop the forks all the way to the ground.

D.  All of the above.

- What is the best way to handle obstructed (blocked) vision from a tall load ?

A.  Drive with the load elevated so that you can see under it.

B.  Drive only in familiar territory and use the horn a lot to warn people.

C.  Lean out of the side of the forklift so that you can see around the load.

D.  Look behind you while driving in reverse until you reach the drop off.

II. TRUE OR FALSE (Circle T or F whichever is more correct)

- Always drive with your foot resting on the clutch so you can shift faster.	T  F

- Plugging is the preferred method of changing direction (as well as stopping) on

both propane-powered and battery-powered forklifts.		T  F

- When traveling with a load, you should keep the mast tilted back slightly and

the load as low as possible. 	T  F

- It’s okay not to look behind you when backing up just a few feet.    		T  F

- Since the rear wheels guide the turning of the truck, the rear end of the truck will

tend to swing wide in a turn.		T  F

- A good driver will develop the habit of making fast, sharp turns for efficiency.		T  F

- Use the forks of a forklift only for picking up loads -- never for pushing, shoving

or ramming. 		T  F

- If the lift mechanism of the forklift makes a strange noise while using it, you should

tell your supervisor about it after you have finished your shift. 		T  F

- Pedestrians and fellow workers are responsible for keeping within their own traffic

lanes and out of the way of your truck.		T  F

- Racing the engine is a good way to warm up your propane-powered forklift quickly.	T  F

- I will always wear a seat belt when operating this equipment.		T  F

- The horn is a 360-degree warning device to others nearby.		T  F

- The forks or guard should be used to bump a loaded pallet into position.		T  F

- If you took a sharp right turn, centrifugal force will cause the combined center

of gravity to shift to the left momentarily.		T  F

- I will follow guidance given to me from all supervisors, forklift trainers,

and the Safety Coordinator.		T  F