# SAFETY OPERATING PROCEDURES

Chainsaw - Electric

Student use of this machine will require direct supervision

### PRE-OPERATIONAL SAFETY CHECKS

- Do not use an electric chainsaw in wet conditions.

- Faulty equipment must not be used.  Report suspect machinery immediately.

- Ensure that the machine and extension cord are tested and tagged for currency.

- Ensure the extension cord is in good condition.

- Ensure a tagged and tested RCD is used when operating the machine.

- Trip test the RCD before use.

- Ensure that chain guard and chain brake are functioning.

- Ensure chain is sharp and correctly tensioned.

- Ensure that safety harness, if required, is in sound condition.

#### OPERATIONAL SAFETY CHECKS

- Maintain a proper balance and secure footing.

- Keep a firm grip on the chainsaw with both hands, with the thumb of the hand holding the front handle wrapped around the handle.

- Start the cut with the saw chain rotating at full speed and the spiked bumper in contact with the wood.

- Pay full attention to the operation and be alert for movement of the material being cut.

- Be aware of the guidebar nose at all times when the saw chain is in motion.

- Be alert to situations that may cause material to pinch the top of the saw chain.

- Avoid the accumulation of debris.

- Ensure that no person or animal is endangered when operating equipment.

#### HOUSEKEEPING

- Remove any foreign material from motor and guards.

- Keep the work area and implement shed in a clean and tidy condition.

## POTENTIAL HAZARDS

  - Kick-back							(	Push-back			(	Pull-in

  - Rotating chain					(	Flying debris		(	Trip hazards

  - Loose clothing entanglement 	(	Noise