# SAFETY OPERATING PROCEDURES

Vehicle Hoist

DO NOT use this machine unless a teacher has instructed

you in its safe use and operation and has given permission.

| Safety glasses must be worn at all times in work areas. | Long and loose hair must be contained. |
| --- | --- |
| Appropriate footwear with substantial uppers must be worn. | Close fitting/protective clothing must be worn. |
| Rings and jewellery must not be worn. | Do not stand on hoist whilst hoist is in operation. |

A vehicle hoist must not be operated unless it has a current certificate of inspection.

### PRE-OPERATIONAL SAFETY CHECKS

- Ensure that vehicle hoist has operating and maintenance instructions permanently located and clearly visible.

- The equipment must be used in accordance with manufacturer’s instructions.

- Check the capacity of the hoist compared to the weight of the vehicle. If vehicle is too heavy, do not proceed.

- Ensure the area is clean and clear of grease, oil, and objects that may be a slip/trip hazard.

- Familiarise yourself with and check all machine operations and controls.

- Check all safety devices are in good condition.

- Ensure support arms are capable of being locked in position.

- Ensure rubber pads are in good condition on all load points.

- Faulty equipment must not be used. Immediately report suspect equipment.

#### OPERATIONAL SAFETY CHECKS

- Centre vehicle on hoist, ensuring that the weight is evenly distributed to the front and rear.

- Identify the correct jacking points and place the lifting pads under the vehicle at the front & rear on the jacking points, ensuring contact.

- Only one person shall operate the hoist at a time.

- Ensure hoist area is clear of people and equipment before operating.

- Never leave the hoist running unattended.

- Check vehicle stability by looking at the jacking points.

- Engage manual lock.

- At the completion of work lower the vehicle hoist and ensure all equipment is left in a safe position.

#### HOUSEKEEPING

- Switch off equipment.

- Leave the equipment and work area in a safe, clean and tidy state.

## POTENTIAL HAZARDS

(	Falling objects	(	Trapping hazards 	(	Crushing hazards (	Entanglement hazards